2020 4 Cylinder Division Rules

CAR ELIGIBILITY

- 1966 and newer

- American or Foreign

- Front wheel and rear wheel drive

  - Three or four-cylinder

  - Non-turbo charged

  - No carburetor adapter plates

- Passenger cars, station wagons, and compact trucks

- Four-wheel drive trucks are allowed if one drive shaft is disconnected (either front or rear)

- MINI-VANS ARE LEGAL

- No 2-seaters (e.g. Fiero’s, Honda CRX)

- No convertibles

- Maximum wheelbase is 104 inches

  - Exception of station wagons and pickups.

ROLL BARS/CAGE

- Minimum 6-point cage is mandatory (full cage recommended),

  - Constructed of at least 1.5-inch OD, .095-inch side wall roll car steel tubing (seam split resistant, cold rolled or seamless; see anyone experienced in building roll cages).

    - No exhaust pipe tubing or water pipe!

  - Cage must be welded or bolted to the floor pan. It is highly recommended that roll cage be welded with 1/8-inch steel plate and bolted to the floor pan using double plate underfloor pan.

    - MAKE ROLL CAGE A PART OF YOUR CAR!

- Driver’s door protection will consist of at least three roll bar type bars welded to roll cage and covered with a minimum 18-inch by 24-inch by 1/8-inch thick steel plate or 18-inch by 24-inch by 1/3-inch aluminum plate.

- Footplates are to be 10-inch by 30-inch by 1/3-inch aluminum are required.

- No offset cages.

- ROLL CAGES ARE SUBJECT TO TECH/TRACK OFFICIALS APPROVAL AND THEIR DECISIONS ISFINAL. CAGES WILL BE TECHED.

BODY/CHASSIS

- Body and frame must match the same make and model.

- Front and rear firewalls must be original and in stock locations.

- All holes and openings in the firewalls must be covered in metal

- No pedal extensions that places the driver behind the b-pillar. (tech’s discretion)

- All body panels will remain stock from front to rear with exception of front nose cover.

- All glass, interior and exterior, must be removed.

- Cars must have full windshields in good condition. Approved Lexan only if there is a full cage. Three minimum 1/8-inch steel bars required with 4-inch spacing with Lexan.

- Doors must be chained or welded shut; WELDING IS HIGHLY RECOMMENDED!!

- Any car with a hatchback can weld or bold the hatchback solid.

- Hood and trunk must be secured with hood pins for easy accessibility; OEM latches must be removed or disabled.

- Fenders may be trimmed (if not excessive) to remove rust out. Excessive cutting and removing of body metal will see the car in question subject to weight penalties as tech/track officials see fit.

- Bumpers may be welded into place. Bumper ends may be capped and have supplemental attachments to the fenders which prevents the hooking of bumpers.

- Non-functional hood scoops are allowed.

- FRONT AND REAR TOW HOOKS OR CHAINS ARE MANDATORY!

- Rub rails allowed. Maximum 1” by 2” rectangle tubing.

- Rear spoilers are not allowed.

BATTERY

- The battery may remain in the original factory location provided it is in a safe location and securely mounted.

- If the battery is relocated

  - Relocated to the trunk area

  - Batteries mounted in the trunk area must be secured by two 1” metal straps.

- No batteries mounted in driver’s compartment.

- Master shut off switch to main battery cable must be placed near driver

  - Preferably on the A pillar for easy access by driver and safety crew is mandatory

COOLING SYSTEMS

- Any stock radiator allowed which will fit in the stock brackets.

- 180-degree fan shroud required.

- No anti-freeze; water only in radiator.

ENGINE

- Engines must be stock for make, model and year of car. No mixing and matching.

- Intake, throttle body and carburetor must be factory stock.

- All cars must pull 18# of vacuum at 1000 RPM hot or cold.

- No altering or add-ons to electronics. MUST BE STOCK. See tech if you are required to replace an item in this area.

- Water pump must remain stock and intact.

BRAKES

- Must have 4-wheel hydraulic brakes in working order

FIRE EXTINGUISHERS

- Each vehicle must be equipped with a charged 2-pound minimum BC rated steel fire extinguisher with gauge

- Mounted in an approved quick release bracket within reach of driver.

  - NO duct tape or zip ties will be allowed.

FUEL TANKS

- Cars without the fuel pump mounted in the tank must use a cell or marine type tank mounted in the trunk floor with a minimum of two (2), 1 inch by 1/16-inch straps in each direction, bolted through the floor using double plates or installed in a safely constructed manner between the frame rails.

- Trunk mounted tanks must be sealed off from the driver’s compartment by a metal plate.

- No bottom draw tanks.

- Maximum 8 gallons.

- Cell required on wagons.

- Cars equipped with electric fuel pumps

  - Must install a toggle type switch,

    - Clearly marked in a bright contrasting color,

    - Mounted at the base of the driver’s “A” pillar.

- If fuel tank is in front of rear axle you can leave it stock.

MUFFLER

- Removal of catalytic converter allowed.

- Loss of muffler will be grounds for black flag.

- Maximum 100 Db at 100 feet.

- Headers are allowed.

SEAT BELTS / SEATS

- Minimum three-inch-wide

- Five-point safety belt assembly required

- Must be mounted securely to the role cage.

- BELTS ARE TO BE NO MORE THAN FIVE YEARS OLD. TRACK OFFICIALS decision is final

- Race seats secured with 3/8-inch bolts are mandatory.

- All seats and belts are subject to tech.

- Officials approval; tech decisions are final!

STEERING AND SUSPENSION

- Must be factory stock or stock replacement, in stock location, with no alternations and must match make and model.

- No adjustable struts/shocks.

- Hex wheel is permitted.

- Power steering is optional.

- Maximum 1” rear steer allowed. Measured from front hub center to rear hub center, per side.

- Maximum 1 ½” camber allowed at all four wheels.

TRANSMISSION

- Stock automatic & stick shifts only.

- Stock converter with no alterations for automatics. OEM style clutch for manuals.

- Must have working forward and reverse gears.

WEIGHT

- Minimum 2400 lbs. All cars will be weighed following the feature, with the driver in-car and in race trim.

- Added weight must be securely fastened

  - Minimum 1/2inch bolts

  - Painted white and include the car’s number on them.

- Weight will be added as deemed necessary by tech officials to maintain parity in the class.

- Tech officials will determine where and how much weight will be added in these cases

NOTE** Bring extra weight with you to the track. Weight may be added for rules infractions or to maintain parity in the class.

- Weight will be added to the car based on its last scaled weight NOT minimum weight of the division.

WHEELS/TIRES

- Stock OEM tires.

  - MUST BE DOT

- 60, 65 or 70 series radial tires allowed.

- No made for racing tires

  - Hoosier, Goodyear or American Racer racing tires).

  - No Falcons.

  - No directional tires.

- All 4 tires must have same size wheel.

- 1” lug nuts recommended.

- No aluminum wheels allowed.

- Off-set racing rims are permitted. (steel only). Any excessive track widths, as determined by track officials, will not be allowed.

- NO TIRE SOAKING ALLOWED